## Slide 1: `
Practical Automated Video Analytics for Crowd Monitoring and Counting
K. H. Cheong, S. Poeschmann, J. W. Lai, J. M. Koh, U. R. Acharya, S.C.M. Yu, and K. J. W. Tang, “Practical automated video analytics for crowd monitoring and counting,” IEEE Access, vol. 7, pp.183252-183261, Dec. 2019.
Presenter: Ashish Kumar
Advisor: Prof. Yo-Ping Huang

## Slide 2: CONTENTS
Proposed work
Introduction
  Object recognition
  Temporal tracking
  Subject counting
  Data processing and computational resource
Results
Conclusion

## Slide 3: PROPOSED WORK
Authors proposed here a low-cost and efficient approach that integrates use of computational object recognition to perform fully-automated identification, tracking and counting of human traffic on camera video streams.

## Slide 4: INTRODUCTION
Why we need automated surveillance systems?
Authors here used a background subtraction scheme and a convolutional neural network based single shot detector (SSD).
Authors developed a software solution for used in general public spaces and validate performance of platform through indoor controlled and outdoor non-controlled tests.
Software package was implemented on python with open source computer vision (OpenCV) library.

## Slide 5
Authors used footage of 720p at 30fps in the paper.
Pre-existing video surveillance system
Centralized storage pool
Footage pulled for real time analysis

## Slide 7: OBJECT RECOGNITION
Background subtraction (BGS)
Detecting moving objects from stationary camera placement.
Background frame is common and subtracted from each frame of video footage.
Mixture of Gaussians (MOG) – BGS based object recognition framework used Gaussian mixture background/foreground segmentation algorithm.
MOG2 provide better human subject identification and segmentation results than MOG and GMG.

## Slide 8
Process utilized for incoming frames:
Brightness and colour correction filter – adjusting under or over exposure or changing daylight conditions.
Noise reduction – improving image quality.
BGS mask is computed and applied through MOG2.
Contours on masked image identified through contrast segmentation to extract boundary boxes and positions of human subjects.

## Slide 11
Convolutional Neural Networks (CNN)
Both YOLO and SSD methods were compared.

## Slide 12
Model utilized in paper is implementation of Google’s MobileNet SSD.
Initially trained on common objects in context (COCO) dataset and refined on PASCAL VOC0712.

## Slide 13: TEMPORAL TRACKING
Comparing the centroids of identified boundary boxes for each frame against those of previous and labelling pairs as identical based on nearest distance basis.
Centroid in previous frame
No matching counterpart in current frame
Left the scene
Centroid in current frame
No matching counterpart in previous frame
Newly entered

## Slide 14
Checked at reference marked wrong in research paper

## Slide 15: SUBJECT COUNTING
Counting of identified objects can be set to scene wise or portal wise.
Scene wise – subjects are counted the movement they enter scene captured by video camera and real time on-scene subject counts are recorded together with cumulative counts.
Extreme boundaries between which counting occurs and subject tracking take place.
Portal wise – subjects are added to cumulative count only when they cross a specified boundary in the captured scene.
User may select from default preset of 10 regularly spaced boundary lines or freely draw desired boundary.

## Slide 16: DATA PROCESSING AND COMPUTATIONAL RESOURCE
Program was configured to perform BGS or SSD every N0 frames.
Subject tracking and counting is set to occur every N0 = 6 frames corresponding to 200ms refresh rate.
Laptop - Intel I5 8250U quadcore processor at 1.6 GHz, 8 GB of RAM, and an Intel UHD Graphics 620 graphics processor, running the Ubuntu (Linux) OS.

## Slide 17: RESULTS
Controlled Environment

## Slide 19
Each test lasted a duration of 150 seconds with both the BGS and SSD methods and manual on-site counting was performed simultaneously to match the results.
BGS achieved perfect accuracy in idealized single subject scenario but ultimately outperformed by SSD in more realistic multiple subject scenario.
SSD yielded maximum of single miscount in controlled tests.

## Slide 20
Uncontrolled Environment

## Slide 23: CONCLUSION
A number of classical and CNN based object recognition techniques for real time video analytics is shown and software platform developed implementing BGS and SSD methods is suitable for deployment for crowd monitoring in public spaces.
Results indicate good accuracy of SSD system even in outdoor conditions.
Proposed video analytics can enable significant manpower savings and better data collection of crowd density and movement can be performed more consistently with better accuracy.

## Slide 24
Software solution developed can accept multiple video stream from centralized storage location suitable for operation in facilities management or public spaces with multiple installed security cameras.

## Slide 25
Thank You